## Slide 1: OBJ to binary structure
File structure
V1.2
G. Dumitra

## Slide 2
History
version | changes
1.0 | Define OBJ structure
1.1 | Define MTL structure
1.2 | Update MTL structure with the support for the Map_Ke parameter

## Slide 3
Summary
How to export from Blender to OBJ
  Known limitations of Blender
  Example of exporting settings
Internal file structure
MTL structure
  Known limitations: MTL structure
OBJ structure

## Slide 4
At this date [2021-10-06] the following limitations are known according to https://docs.blender.org/manual/en/latest/addons/import_export/scene_obj.html?highlight=mtl
How to export from Blender to OBJ: Known limitations of Blender
The OBJ format is a popular plain text format, however, it has only basic geometry and material support.
Mesh: vertices, faces, edges, normals, UVs
Separation by groups/objects
Materials/textures
NURBS curves and surfaces
Note
There is no support for:
Mesh vertex colors
Armatures
Animation
Lights
Cameras
Empty objects
Parenting
Transformations.

## Slide 5
In order to have the OBJ and MTL files compatible with this parser you need to export from Blender with the triangulate faces option check!
How to export from Blender to OBJ: Example of exporting settings

## Slide 6
Internal file structure
MTL Information Array of Material(s)
Array of Face(s) (triangles)
Array of materials
Array of vertices
MTL material ID (or -1 in case of none) <signed short>
n
n

## Slide 7
Internal file structure: more details
MTL Information Array of Material(s)
Array of Face(s) (triangles)
MTL ID
Items no.
1..n
MTL ID
Items no.
1..n
No of materials <signed int>
Material name
<array of signed chars>
No of chars <short>
“is KA ?” Bool 0 or 1 <byte>
X,Y,Z coordinates
Array of float [3]
Array of materials
Array of vertices

## Slide 8
Array of materials: MTL structure
No of materials <signed int>
Material name
<array of signed chars>
No of chars <short>
“is KA ?” Bool 0 or 1 <byte>
“is KD ?” Bool 0 or 1 <byte>
X,Y,Z coordinates
Array of float [3]
X,Y,Z coordinates
Array of float [3]
“is KS ?” Bool 0 or 1 <byte>
X,Y,Z coordinates
Array of float [3]
“is KE ?” Bool 0 or 1 <byte>
X,Y,Z coordinates
Array of float [3]
Ns <float>; “-1” => not available
Ni <float>; “-1” => not available
d <float>; “-1” => not available
illum <byte>; “-1” => not available
0
Map_ka file name
<array of signed chars>
No of chars <short>
Map_kd file name
<array of signed chars>
No of chars <short>
Map_ks file name
<array of signed chars>
No of chars <short>
Map_ns file name
<array of signed chars>
No of chars <short>
Map_d file name
<array of signed chars>
No of chars <short>
One material unit
Map_ke file name
<array of signed chars>
No of chars <short>
Map_Bump file name
<array of signed chars>
No of chars <short>
bm <float>

## Slide 9
No of triangles/faces units <signed int>
X,Y,Z coordinates
Array of float [3]
U,V coordinates(*)
Array of float [2]
“is U,V ?” Bool 0 or 1 <byte>
Only if “U,V” value=1 
“is Normal?” Bool 0 or 1 <byte>
Only if “is Normal” value=1 
X,Y,Z normal
Array of float [3]
X,Y,Z coordinates
Array of float [3]
U,V coordinates(*)
Array of float [2]
“is U,V ?” Bool 0 or 1 <byte>
Only if “U,V” value=1 
“is Normal?” Bool 0 or 1 <byte>
Only if “is Normal” value=1 
X,Y,Z normal
Array of float [3]
Obj name
<array of signed chars>
No of chars <signed short>
Array of OBJ/faces: OBJ structure
MTL material ID (or -1 in case of none) <signed short>
No of OBJs <signed int>
One vertex unit
0

## Slide 10
Parametes and known limitations:
MTL parser
  Ka = “ambient reflectivity” (material ambient is multiplied by the texture value)
    Only “Ka r g b” is supported. Same for “Kd” and “Ks”
      Not supporting “Ka spectral file.rfl factor”
      Not supporting “Ka xyz x y z”
    map_Ka (!! see “2. MTL structure” for limitations !!)
      Specifies that a color texture file or a color procedural texture file is applied to the ambient reflectivity of the material. During rendering, the "map_Ka" value is multiplied by the "Ka" value.
  Ks = “specular reflectivity”
    map_Ks (!! see “2. MTL structure” for limitations !!)
      specular reflectivity of the material (value is multiplied by the "Ks" value)
  Kd = “diffuse reflectivity”
    map_Kd (!! see “2. MTL structure” for limitations !!)
      diffuse reflectivity of the material (value is multiplied by the "Kd" value)
  Ke= “emissive coeficient”
    It goes together with ambient, diffuse and specular and represents the amount of light emitted by the material. If you also have a defined emission color the material will irradiate light.
    map_Ke (!! see “2. MTL structure” for limitations !!)
      diffuse reflectivity of the material (value is multiplied by the "Ke" value)
  map_Bump = Specifies that a bump texture file is linked to the material. To be see how this is working against the normal.
    Supported parameters: only bm = float [0.0…1.0]

## Slide 11
Parametes and known limitations:
MTL parser (continue)
  Illum = “specifies the illumination model to use in the material” (hint: search for “The illumination models are:” http://paulbourke.net/dataformats/mtl/)
    0 Color on and Ambient off
    1 Color on and Ambient on
    2 Highlight on
    3 Reflection on and Ray trace on
    4 Transparency: Glass on; Reflection: Ray trace on
    5 Reflection: Fresnel on and Ray trace on
    6 Transparency: Refraction on; Reflection: Fresnel off and Ray trace on
    7 Transparency: Refraction on; Reflection: Fresnel on and Ray trace on
    8 Reflection on and Ray trace off
    9 Transparency: Glass on; Reflection: Ray trace off
    10 Casts shadows onto invisible surfaces
  d factor = “the amount this material dissolves into the background. A factor of 1.0 is fully opaque. This is the default when a new material is created. A factor of 0.0 is fully dissolved (completely transparent).”
  Sharpness = not supported
  Ns = specular exponent for the current material. Values = 0..1000
  Ni = Specifies the optical density for the surface. Values = 0.001..10 (usually values are >1.0)
  Note:
  - Ka - material ambient is multiplied by the texture value
  - Kd - material diffuse is multiplied by the texture value
  - Ks - material specular is multiplied by the texture value

## Slide 12
Known limitations:
2. MTL structure: map_ka, map_kd are supported without “options”: Examples:
  OK => “map_Ka mapfile.png”
  NOK => “map_Ka -s 1 1 1 -o 0 0 0 -mm 0 1 chrome.mpc” (program will crash!)
  Options that are not supported (according to http://paulbourke.net/dataformats/mtl/ )
    -blendu on | off
    -blendv on | off
    -cc on | off
    -clamp on | off
    -mm base gain
    -o u v w
    -s u v w
    -t u v w
    -texres value
3. All strings are US-ASCII

## Slide 13: Example
Take as an example the already serialized file “/examples/cube_output.bin”

## Slide 14
Structure Example:
According to the definition of the file structure from page 5, we are looking first for the number of materials used by the object.
The file starts as:
No of materials <signed int>
This means we have 2 materials we shall load into memory.